## Slide 1
Sulfur Oxidizing Bacteria Biosensor: Principles & Applications
Dr. Sedky .H.A. Hassan
Botany & Microbiology Dept.
Faculty of Science, New Valley University
Egypt
Email: sedkyhassan@aun.edu.eg
By

## Slide 2
INRODUCTION
Contamination
of
Environment
Chemical assays
&
Biological
Methods
Rapid
Industrialization
Introduction

## Slide 3
Chemical assay
INRODUCTION

## Slide 4
Toxicity Bioassay
Bioassay Methods
Eukaryotic
Prokaryotic
INRODUCTION

## Slide 5
Fish
Mortality or movement direction
ATP
Survival
Some fish are not sensitive to low concentration,
Test take some days
Tolerate pollutants and they need specialized equipment and operators with adequate skills
INRODUCTION

## Slide 6
Daphnia & Shrimp
Mortality or motlity, cell count, speed variation
Operator skills, less senstivity
INRODUCTION
High sensitivity to toxicants, simplicity, short exposure duration, short reproductive cycle and parthenogenetic reproduction

## Slide 7
Snails
INRODUCTION
Mortality
Open and closed of shell
Egg production
Less sensitivity to low concentration
Operator skills

## Slide 8
Algae bioassay
The growth of the algae exposed to the test substance is compared with the growth of the algae in an appropriate control over a fixed period of time under defined conditions.
Mortality or photosynthesis activities
Algal growth
enzymatic activity
cell count
INRODUCTION

## Slide 9
Plants bioassay
Chinese cabbage, oats
Vicia faba, Allium cepa
Micronucleus, genotoxic
germination rate, biomass weight,
enzyme activity
Require a long time for growth to occur, e.g., 4-6 days for length measurement of root and shoot of the plants, 14-30 days for fresh or dry weight measurement and 21 days for germination scores.
INRODUCTION

## Slide 10
5
1
Quickly, easily detection protocol,
2
Less time consuming
3
Inexpensive
4
More sensitive
Short life cycle
Microbial Bioassay Advantages
INRODUCTION

## Slide 11
1
Monitoring in the growth rate
2
Biochemical properties, mortality
3
Capacity of microorganisms to transform carbon, sulfur or nitrogen
4
Bioluminescence
5
Photosynthetic activity
Microbial Bioassay based Mechanism
INRODUCTION

## Slide 12
7
Nitrification inhibition
8
Enzyme activity and inhibition
9
Fluorescence of chlorophyll
10
Respiration, oxygen consumption
Microbial Bioassay based Mechanism
INRODUCTION

## Slide 13
Aerobic bacteria
Bioluminescent bacteria
Algae
Nitrifying bacteria
Bacteria in microbial fuel cells
Activated Sludge
Genetic engineered bacteria
Photobacterium phosphoreum
Vibrio fischeri
Iron oxidizing bacteria
Oligotrophic bacteria
Yeast
Microorganisms
INRODUCTION

## Slide 14
Bioluminescence, bacterial growth
INRODUCTION

## Slide 15
1
Need special instrument such as spectrophotometer, respirometer, photometer, microtox….etc.
2
Work at neutral or high pH
3
Contamination
4
Need training person
Some disadvantages

## Slide 16
Biosensors are analytical devices, constructed by combining a biological sensing element (e.g., enzymes, antibodies, microorganisms or DNA) with a transducer (e.g., electrochemical, optical, thermal) to obtain signal output.
Biosensors?
INRODUCTION

## Slide 17
Reliable and reproducible;
Economical of time and resources;
Relevant, practicable and readily understood by the layman;
Validated
Simple to use and specifiec.
Useful for large monitoring analysis
With a clearly defined end-point;
Sensitive to a wide range of pollutants.
Response to low concentration of pollutants.
An ideal biosensor should be:
INRODUCTION

## Slide 18
Signal
Transducer
Analyte
S
P
A whole-cell biosensor contains living organisms, such as bacteria, microalgae, yeast or fungi as the sensing elements through transducer (release ions, H+, light emission). The transducer convert biological signal into measurable response such as current or voltage or conductivity.
Microbial Biosensor
INRODUCTION

## Slide 19
Microbial Biosensor
INRODUCTION

## Slide 20
Sulfur Oxidizing Bacteria
So + H2O + 1.5 O2 → SO42- + 2H+
In presence of toxic chemicals
The activity of SOB will be inhibited, which will cause an increase in pH and a decrease in EC.
OBJECTIVE
Oxidation of S results in the formation of sulfuric acid (SO42- and H+) which lowers the medium pH.
The production of sulfate ions increases the electrical conductivity (EC) of the medium

## Slide 21: MCR
Operating conditions
NMB media (100 X)
Inoculum: SWW
Sulfur particles (2-4 mm)
Air flow rate (150-200ml/minutes)
Temperature 30 °C
MATERIALS & METHODS

## Slide 22: A schematic diagram of Sulfur Oxidizing Bacteria Biosensor
MATERIALS & METHODS

## Slide 23: Continuous Monitoring system
Sulfur particles
(2
-
4mm)
Air
pH probe
EC probe
Influent
Effluent port
Computer
Pump
Sulfur particles: 2-4 mm
Volume: 50 ml of sulfur
Medium: NMB medium diluted to 100 times
Influent EC 0.14 mS/cm, pH 6.9
HRT: 30 mints
Time intervals: 10 mints
Temp: 30 ºC
MATERIALS & METHODS

## Slide 24: Batch mode
Operating conditions
Sulfur particles: 2-4 mm
Volume: 50 ml of sulfur
Medium: NMB diulted 100 times
Initial EC 0.12 mS/cm,
pH 6.9
Time intervals: 10 mints
Temp: 30 ºC
Operation: Batch mode
RESULTS

## Slide 25
Operating conditions
Sulfur particles: 2-4 mm
Volume: 50 ml of sulfur
Medium: Stream water
Influent EC 0.14 mS/cm,
pH 6.9
HRT: 30 mints
Time intervals: 10 mints
Temp: 30 ºC
Steady state
RESULTS

## Slide 26
Detection of Cr6+ by SOB biosensor.
RESULTS

## Slide 27
Toxicity of CN-
RESULTS
Operating conditions
Sulfur particles: 2-4 mm
Volume: 50 ml of sulfur
Medium: NMB diulted 100 times
Initial EC 0.12 mS/cm,
pH 6.9
Time intervals: 10 mints
Temp: 30 ºC
Operation: Batch mode

## Slide 28
Toxicity of heavy metals
RESULTS

## Slide 29
Mixture of heavy metals
Operating conditions
HRT: 30 min
Sulfur particles 2-4, mm)
Mixture of heavy metals (Cd2+, Pb 2+, Hg 2+ was added after 5 hours.
Conc: 50 ppb
RESULTS

## Slide 30
99.8 % of bacterial count was autotrophic SOB
0.2 % of bacterial count was heterotrophic bacteria
SOB bacteria
RESULTS

## Slide 31
Character | Results | Character | Results | Character | Results
Morphology | flat, small, white | Arabinose | - | Orinithine | -
Gram stain | - | Sorbitol | - | Tryptophan | -
Indole | - | Inositol | - | Lactose | -
H2S | - | Orinithine | - | D-fructose | -
Urease | - | Saccarose | - | L-lysine | -
VP | - | D-Glucose | - | Citrate | -
Mannose | - | D-xylose | - | Autotrophs | +
Gelatin | - | D-galactose | - | Mixotrophic | +
Amyadalin | - | D-mannose | - | Heterotrophic | -
SOB bacteria
RESULTS

## Slide 32
RESULTS
Endocrine disruptors (EDCs)

## Slide 33
RESULTS
Endocrine disruptors (EDCs)

## Slide 34
SMCR
RESULTS
Detection of NO2-N (Batch Mode)

## Slide 35
RESULTS
Detection of NO2-N (Batch Mode)
To study the effect of pH, free nitrous acid (HNO2), and alkalinity on SOB Alk (1567 mg/L)

## Slide 36
RESULTS
Detection of NO2-N (Batch Mode)
To study the effect of pH, free nitrous acid (HNO2), and alkalinity on SOB Alk (293 mg/L)

## Slide 37
Detection of NO2-N (Batch Mode)
To study the effect of pH, free nitrous acid (HNO2), and alkalinity on SOB Alk (17.5 mg/L)
RESULTS
pKa (3.1)
Free radicles
HNO2

## Slide 38
RESULTS
Inhibition %

## Slide 39
RESULTS
Detection of NO2-N

## Slide 40
Operating conditions
HRT: 30 min
Sulfur particles
(0.8-1.0, 2-4, 4.0-4.75 mm)
Cr6+ (50 ppb) was added
after 5 hours
RESULTS
Effect of S° particle size

## Slide 41
Operating conditions
HRT: (30, 20, and 10 min).
Cr6+ (50 ppb) was added
after 5 hours of operation.
Effect of HRT
RESULTS

## Slide 42
RESULTS
Operating conditions
HRT: 30 min
Sulfur particles
(2-4, mm)
Different temperatures ( 20, 30, 45, 50, 60 °C)
Effect of temperature

## Slide 43
Operating conditions
HRT: 30 min
Sulfur particles(2-4, mm)
Temp (30, 45 °C)
Cr6+ (50 ppb)
Effect of temperature on Cr6+ detection
RESULTS

## Slide 44
Operating conditions
HRT: 30 min
Sulfur particles(2-4, mm)
Different alkalinities
RESULTS
Effect of alkalinities

## Slide 45
Detection of stream water by SOB biosensor.

## Slide 46
Assessment of industrial effluent by SOB biosensor.

## Slide 47
 | UNIT | C1 | R1 | R2
pH | - | 8.5 | 7.6 | 7.26
EC | mS/cm | 1.25 | 0.2 | 0.23
Ammonia | ppm | 6.7 | 2 | 2.2
NO2-N | ppm | 1.1 | 0.18 | 0.48
NO3-N | ppm | 9.43 | 3.4 | 3.47
PO4- | ppm | 1.58 | 0 | 2.45
1,4 Dioxane | ppm | 0.27 | - | -
Cd | ppm | 0.001 | 0.001 | 0.001
Cr | ppm | ND | ND | 0.001
Cu | ppm | ND | 0.002 | 0.003
Pb | ppm | 0.019 | 0.012 | 0.02
Hg | ppm | 0.002 | ND | ND
Zn | ppm | 0.014 | 0.01 | 0.025
Physicochemical parameters of textile industry effluent and river waters

## Slide 48
RESULTS
Effect of alkalinities
Operating conditions
HRT: 30 min
Sulfur particles(2-4, mm)
Different alkalinities
Cr6+ (50 ppb)

## Slide 49
Conclusions
The methods is consider a new assay for toxicity assessment.
SOB biosensor detect toxic chemicals in different mode.
SOB biosensor can be improved by changing HRT or increasing sulfur particles size.
Detection of many toxic chemicals.
CONCLUSIONS

## Slide 50
SOB biosensor detect toxic chemicals in industrial effluents.
Recovery after toxicity.
Can be operated at different temperature
The sensitivity to detect toxic chemicals increase at low alkalinity.
Conclusions
CONCLUSIONS

## Slide 51
Simplicity
Sulfur is cheap
High sensitivity
Easy operation
Different mode
No Contamination
No specific media
No calibration needed
Operation for long time
Ability to monitor toxicity in real-time
Minimize the formation of complexes (low pH)
Eco-friendly
Advantages of SOB
CONCLUSIONS

## Slide 52: PATENTS

## Slide 54: شكرا لحسن الاستماع